## Slide 1
Design of a 4:1 Multiplexer and Extension to an 8:1 Multiplexer
Subject: Digital Logic Design
Team Members
1. B. Bhuvan Sai Teja
2620030671
2. S. Bhavya
2620090008
3. K. Meghana
2620090020
4. K. Saketh
2620090009

## Slide 2
Introduction to Multiplexers
2
A multiplexer (MUX) is a digital switch
It selects ONE input from many inputs
The selected input is sent to ONE output
Select lines decide which input is chosen
Data Inputs
The signals to choose from
Select Lines
Pick the input
Output
Carries the chosen signal
Real-Life Example
📺
Choosing a TV channel:
• Many channels = inputs
• Remote buttons = select lines
• Screen = output
Only ONE channel shows at a time.

## Slide 3
Basic Block Diagram of a Multiplexer
3
I0
I1
I2
In-1
⋮
MUX
2ⁿ : 1
Y
Select lines S0 … Sn-1
Inputs
Inputs: data signals (I)
Select lines (S) choose one input
Output (Y) = selected input
n select lines → 2ⁿ inputs
We will design: 4:1 MUX (2 select lines) and 8:1 MUX (3 select lines)

## Slide 4
Design of a 4:1 Multiplexer
4
I0
AND
I0·S1'·S0'
I1
AND
I1·S1'·S0
I2
AND
I2·S1·S0'
I3
AND
I3·S1·S0
OR
Y
S1, S0 (with NOT gates for S1', S0') go to every AND gate
Data inputs: I0, I1, I2, I3
Select lines: S1, S0
NOT gates make S1' and S0'
Each AND gate passes its input only for its select code
OR gate combines the four AND outputs into Y

## Slide 5
Truth Table of a 4:1 Multiplexer
5
S1 | S0 | Output Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
I0–I3 can be 0 or 1. Y copies the selected input.
S1 S0 = 00 → I0 goes to Y
S1 S0 = 01 → I1 goes to Y
S1 S0 = 10 → I2 goes to Y
S1 S0 = 11 → I3 goes to Y
Example: S1 S0 = 10, I2 = 1 → Y = 1 (other inputs are ignored)

## Slide 6
Boolean Expression and Working of a 4:1 MUX
6
Y = I0·S1'·S0' + I1·S1'·S0 + I2·S1·S0' + I3·S1·S0
Each term has one input and one select code
S1'·S0' is 1 only when S1 S0 = 00, so only the I0 term can pass
S1'·S0 is 1 only for 01 → I1 passes
S1·S0' is 1 only for 10 → I2 passes; S1·S0 is 1 only for 11 → I3 passes
All other terms become 0, so OR gives Y = selected input
Example: S1 S0 = 01
Term I1·S1'·S0 = I1·1·1 = I1
Other terms = 0
Y = 0 + I1 + 0 + 0 = I1

## Slide 7
Introduction to an 8:1 Multiplexer
7
I0
I1
I2
I3
I4
I5
I6
I7
8:1
MUX
Y
S0
S1
S2
8 data inputs: I0 to I7
3 select lines: S2, S1, S0
1 output: Y
Why 3 select lines? 3 bits give 2³ = 8 different codes
Each code (000 to 111) picks one input

## Slide 8
Extending a 4:1 MUX to an 8:1 MUX
8
I0
I4
I1
I5
I2
I6
I3
I7
4:1 MUX
(A)
4:1 MUX
(B)
S1 S0
Y1
Y2
2:1
MUX
0
1
S2
Y
I0–I3 → MUX A
I4–I7 → MUX B
S1, S0 → both 4:1 MUXs
A and B outputs → 2:1 MUX
S2 selects: 0 = A, 1 = B
S1 and S0 choose inside each group; S2 chooses the group.

## Slide 9
Working and Applications
9
Example: S2 S1 S0 = 101
S2 = 1 → 2:1 MUX picks MUX B (I4–I7)
S1 S0 = 01 → MUX B picks its 2nd input
That input is I5
So Y = I5
Select code 101 = decimal 5 → input I5
💾
Data selection
📡
Communication systems
🔌
Digital circuits
🖥️
Processor systems

## Slide 10
Conclusion
10
A 4:1 MUX uses 2 select lines; an 8:1 MUX uses 3
Select lines pick one input and send it to the output
MUXs reduce the need for separate connections
8:1 MUX = two 4:1 MUXs + one 2:1 MUX
S1, S0 go to both 4:1 MUXs; S2 drives the 2:1 MUX
Thank You
Any Questions?